COLD WEATHER OPERATING PRECAUTIONS

If this machine is used in an unheated area during cold weather, the lubricating grease in the ball bearings can become so thick that the motor will not start up properly or may not reach FULL SPEED.  The start windings in the motor will not turn off until the motor has reached full speed.  The start windings can burn out if they are energized for too long.

IT IS VERY IMPORTANT TO VERIFY THAT THE MACHINE HAS REACHED FULL SPEED!!  Therefore, it is not recommended that the machine be used in an unheated area.

The machine in a warm environment will reach full speed in about 3 seconds!  STARTING TIMES LONGER THAN 6 SECONDS ARE A SIGN THAT THE MACHINE NEEDS TO BE PREHEATED!!

Wissota uses the very best quality electric motor grade ball bearings with premium lifetime lubricating grease.  The bearings also have rubber contact seals inboard and outboard as well as a secondary felt dust shield.

These features coupled with our totally enclosed motor design provides exceptional motor life.  Changes to the grease or shielding for improved cold weather starting would come at the expense of the outstanding longevity Wissota customers have come to expect during the past 50 years.

Please pass this information on to all operators of the machine.