Dust Collection System For Wissota

Model 911 Skate Sharpener

Wissota Skate Sharpeners

Phone:  (952) 417-6611

Visit our Web Site at http://www.wissota.com/

WARNING:  While this dust collector hood will aid in hooking up to dust control systems, operators health should be guarded by wearing an appropriate dust mask.  The filter in the dust control system should be .5 micron or better. Check the condition of your filter regularly and change when necessary.

NOTE:  You will need to position your machine near the right edge of a workbench.  The hose nozzle on the dust collector hood will then hang over the edge of the table and allow access by a hose from a dust control vacuum system.  An alternative would be to cut an access hole in the workbench table for the exhaust hose.

INSTALLATION:

Position the Dust Collection System carefully on the machine.  The mounting strap can be bent to improve alignment.

If your skate sharpening machine does not have pre-drilled holes from the factory to mount this dust hood, you will need to drill two mounting holes into the machine.

Use the holes in the mounting strap as a template to mark the location for the holes in the

machine.  Use a drill the same size as the holes in the mounting strap.

The Dust Collection System can now be hooked up to a dust control vacuum system.  The collector nozzle is sized for a 2” hose.  Too hook up the collector nozzle to your shop vac hose, we recommend using a flexible rubber coupler to connect the 2” adaptor to your shop vac hose size.

Keep a fine bristle shop brush handy to sweep away residual dust into the chute.