Dust Collector Hood For Wissota

Model 911 Skate Sharpener

Wissota Skate Sharpeners

Phone:  (952) 417-6611

Visit our Web Site at http://www.wissota.com/

WARNING:  While this dust collector hood will aid in hooking up to dust control systems, operators health should be guarded by wearing an appropriate dust mask.  The filter in the dust control system should be .5 micron or better. Check the condition of your filter regularly and change when necessary.

NOTE:  You will need to position your machine near the right edge of a workbench.  The hose nozzle on the dust collector hood will then hang over the edge of the table and allow access by a hose from a dust control vacuum system.  An alternative would be to cut an access hole in the workbench table for the exhaust hose.

INSTALLATION:

Position the hood carefully on the machine.  Note that the inside bottom surface of the hood should be slightly below the tabletop surface of the skate sharpener.  The skate holder should not contact the hood if it slightly overhangs the machine tabletop.  The hood and mounting tabs can be bent to improve alignment.

If your skate sharpening machine does not have pre-drilled holes from the factory to mount this dust hood, you will need to drill two mounting holes into the machine.

Use the holes in the dust hood as a template to mark the location for the holes in the

machine.  Use a drill the same size as the holes in the dust hood.  Before drilling be sure

the dust hood will not interfere with the skate holder as caution above !

After tightening the bolts, a bead of silicone caulk could be added to form a good seal

between the machine and hood.

The hood can now be hooked up to a dust control vacuum system.  The collector nozzle

is sized for a 2” hose.  Too hook up the collector nozzle to your shop vac hose, we recommend using a flexible rubber coupler to connect the 2” adaptor to your shop vac hose size.

Keep a fine bristle shop brush handy to sweep away residual dust into the chute.

Dust control vacuum systems start at about $100 for a wet/dry shop vac: try Sears, Home Depot, and Lowes. First class industrial systems can top $1500.  Most shops purchase a decent system for about $400.  Most major full line power tool dealers can provide dust control equipment.  Use .5 micron or better filter.

Contact the Wissota factory for help if needed.