WISSOTA “ELITE” EDGE CHECKER

INSTRUCTIONS:

After sharpening, remove the skate from the skate holder and hold the skate with the blade facing upwards.  Secure the magnetic base of the reference piece to the side of your skate blade*, and next place the magnetic angle piece on top of the skate blade directly in front of the reference piece.  If the skate blade edges are even, the top edge of the magnetic angle piece will be parallel with a single white line on the reference piece from the left side to the right.  If the edges are uneven, the magnetic angle piece will clearly be leaning towards one side or the other.

*The magnetic base of the reference piece should always be placed on the side of the skate blade that rests on the bottom bracket of your skate holder.  So for example, if you sharpen your skates with the heel to the left in your skate holder, when you hold up your skate blade to check for even edges always hold the skate with the heel closer to you.  If you sharpen with the toe of the blade to the left, hold the skate up with the toe end closer to you.

It is recommended to check the skate blade for even edges in 3 different spots: the middle of the blade, halfway to the toe, and halfway to the heel.

The increments of the white calibration marks on the reference piece represent one thousandth of an inch of edge change, or .001”.  The total amount of error can be calculated by adding the total difference in calibration lines from the left side to the right.  Refer to your skate holder manual to make the correct amount of adjustment.

*TOLERANCE: If you are slightly off but still within .001” of an edge change, it is not worth your time trying to adjust for that small of a difference that even a professional skater would never notice.  Ideally we would be able to sharpen perfectly even edges all the way down the blade on every skate that we encounter, however realistically this is just not possible due to the inconsistencies of the skate blades themselves.  Skate Blade manufacturers are just not able to make a piece of steel that is exactly the same thickness and perfectly straight, even for their top of the line blades, which therefore leads to small inconsistencies in edges as well.

Be sure to clean off the skate blade, the bottom of the magnetic angle piece, and the part of the reference piece that secures to the side of your skate blade before checking.

When moving the edge checker to different spots on the skate blade, be sure to lift the whole unit off the blade and place it back on in a different spot.  DO NOT slide the edge-checking tool down the skate blade, as this can damage the bottom of the skate blade.

Questions?

Contact Wissota Skate Sharpeners at (952) 417-6611 or sales@wissota.com

The picture below shows that the edges are off by .002”

The picture below shows even edges.