WISSOTA GRINDING WHEELS

DELIVER THIS SHEET WITH THE GRINDING WHEEL TO THE

OPERATOR

WARNING!

SKATE SHARPENING CREATES DUSTS.  Excessive dust inhalation will adversely affect your respiratory health.  Always consider the material being ground when selecting dust control measures. Wissota cannot control the chemical properties of the steel you will grind.  Therefore, always wear an appropriate, tight fitting DUST MASK when operating the machine.

WARNING!

Skate sharpening presents a risk of serious eye trauma due to flying particles. Always wear EYE PROTECTION before starting the machine and at all times during operation.  This wheel is for use only on Wissota skate sharpening machines. Any other use may present serious personal injury hazards.  Read and understand machine owners manual before starting.

WARNING!

Keep the spark breaker (part #911-20) properly adjusted.  The spark breaker should be kept adjusted to be no more than ¼” distance from the grinding wheel.  In case of wheel breakage during operation, this will prevent large pieces of wheel from being ejected at the operator.  During normal operation, the spark breaker helps contain small debris.  As the grinding wheel wears down to a smaller diameter, loosen the hold down screw (p/n 4005) and slide the spark breaker closer to keep the gap ¼” or smaller.  Retighten screw.  When the gap exceeds ¼” and you can not slide the spark breaker any further, remove the spark breaker, rotate it 180 degrees, and reinstall to a ¼” gap.

# REPLACING THE WHEEL

- Make sure machine is off. To prevent accidental starting, unplug machine from electrical source.

- Remove two red guard-cover knobs. (911-1)

- Lift guard cover (911-2) off machine.

- Hold wheel with one hand to prevent turning. Using a wrench, turn the hex nut counter clockwise

- Remove old wheel. Clean all abrasive build up from the guard and guard cover.

- Install new wheel. Make hex nut (S-4) snug fit only. Do not over tighten.

- Adjust spark breaker. See reverse of this sheet for instructions.

- Do not start machine until eye protection is being worn and until all parts are reassembled and properly adjusted. To guard against abusive handling in transit or during redistribution outside of our plant, stand clear for two (2) minutes before using.

- New wheels have a “flat” un-curved face. Take very light initial dressings of the wheel to remove the top and bottom corners of the wheel smoothly and cleanly.

QUESTIONS? CONTACT THE FACTORY

www.wissota.com		(952) 417-6611