WARNING:  ALWAYS KEEP YOUR HDI OUT OF THE EXHAUST DUST FROM YOUR GRINDING MACHINE

DO NOT ATEMPT TO DISASSEMBLE THE DIAL INDICATOR ITSELF

Cleaning and Maintenance of the HDI

- Unthread and remove black knob and white washer from HDI body

- Pull the HDI body apart

- Remove brass slide plate and dial indicator from HDI body

- Using a Scotch Brite, clean the surface area where the brass slide sits (referred to as the slide bed).  Then use a clean cloth to remove any debris.

- Use a Q-Tip to clean and lubricate the slide bed (where the brass slide plate seats) with a small amount of veg. oil.

- Lubricate the slide pins (the pins that hold the two body parts together) within the body before putting them back together.

- Put HDI body together, return brass slide to slide bed, and replace white washer and black knob.

This process should be done frequently to ensure that parts do not stick or wear prematurely.  Recommend cleaning every two to three weeks, depending on the amount of skates being sharpened and how dusty the sharpening area is.  Remember:  Do not put your HDI where the grinding dust is discharged from the machine.

NOTE:  The contact point will absorb wear which will flatten the radius point.  You will need to replace the contact point from time to time.

Dial Indicator Replacement

NOTE: These instructions are set on a 9’ radius blade (Bauer)

- Remove the faulty dial by using a 5/64 hex wrench.

- Insert the hex wrench into the hex head set screw located in the brass plate.

- Loosen hex head screw two to three turns so that the dial indicator can easily be removed.

- Before installing the new indicator, mount the HDI unit onto a skate blade (9’ rocker) and tighten the black knob.

- Position the brass plate to center position and insert the new dial indicator.

- Slowly  move the brass plate to your left edge of skate blade and very carefully, press down on the new dial indicator until it bottoms out (Dial will be moving in the clockwise direction until it bottoms out or stops.)

- Lift the dial indicator slowly and carefully as the needle or indicator will move in the counter clockwise direction.  Lift until the needle or indicator reaches the twelve o’clock position. Hold securely in this position.

NOTE:  The indicator will move in the counter clockwise direction when you are pulling it up or away from the HDI body and it will move in the clockwise direction when you are setting it down onto the HDI body.

- Square up the face of the dial with the body of the HDI and tighten the hex head set screw with the 5/64 hex wrench. (Located in the brass slide plate).

If you have any questions, whatsoever, please do not hesitate to contact us at 320-815-3338.  Thank you for using the Hollow Depth Indicator manufactured by the skate sharpening experts at Edge Specialties, Inc.